Inteli-Power Specifications Table

|  | PD9245C | PD9260C | PD9270 | PD9280 |
| --- | --- | --- | --- | --- |
| Maximum DC Output Current | 45-AMPS | 60-AMPS | 70-AMPS | 80-AMPS |
| Maximum Continuous Input Power | 725 WATTS | 1,000 WATTS | 1,250 WATTS | 1,300 WATTS |
| No Load DC Output Voltage | 13.6 VDC | 13.6 VDC | 13.6 VDC | 13.6 VDC |
| No Load Voltage Tolerance | +/- .3 VDC | +/- .3 VDC | +/- .3 VDC | +/- .3 VDC |
| Full Load Output Voltage | > 12.6 VDC | > 12.6 VDC | > 12.6 VDC | > 12.6 VDC |
| Ripple and Noise Voltage | <50 MV RMS | <50 MV RMS | <50 MV RMS | <50 MV RMS |
| Input Voltage Tolerance | 105 - 130 VAC | 105 - 130 VAC | 105 - 130 VAC | 105 - 130 VAC |
| Input Voltage Frequency | 50-60 HZ | 50-60 HZ | 50-60 HZ | 50-60 HZ |
| Peak Inrush Current | 32-AMPS | 47-AMPS | 47-AMPS | 80-AMPS |
| Efficiency (Typical) | > 80% | > 80% | > 80% | > 80% |
| Reverse Battery Protection | YES | YES | YES | YES |
| Electronic Current Limiting | YES | YES | YES | YES |
| Variable speed Intelligent Cooling Fan * | Auto-speed | Auto-speed | Auto-speed | Auto-speed |
| Back Up Thermal Protection | YES | YES | YES | YES |
| Storage Temperature | 20-80C | 20-80C | 20-80C | 20-80C |
| Operating Temperature | 0-50C | 0-50C | 0-50C | 0-50C |
| Hipot Voltage Test | <-------------- 1240 V @ INPUT TERMINALS ------------> |
| Accessory Port for optional Pendant** | Standard | Standard | Standard | Standard |
| Weight | 4.5 LBS. | 5.8 LBS. | 5.8 LBS. | 7.5 LBS. |
| Dimensions | 8.25"L X 7.25"W X 4.5"H | 8"L X 9.00"W X 3.6"H | 8"L X 9.00"W X 3.6"H | 11.5"L X 9.00"W X 3.6"H |
| UL & c UL Listed | YES | YES | YES | YES |