PD4000 Mighty Mini Inteli-Power Panel Specifications Table

PD4045 Maximum DC Output Current 45-AMPS Maximum Continuous Input Power 725 WATTS No Load DC Output Voltage 13.6 VDC No Load Voltage Tolerance +/- .3 VDC Full Load Output Voltage > 12.6 VDC Ripple and Noise Voltage <50 MV RMS Input Voltage Tolerance 105 - 130 VAC Input Voltage Frequency 50-60 HZ Peak Inrush Current 47-AMPS Efficiency (Typical) > 80% Reverse Battery Protection YES Electronic Current Limiting YES Cooling Fan Auto-variable speed Back Up Thermal Protection YES Full Function Charge Wizard YES Storage Temperature 20-80C Operating Temperature 0-50C Hipot Voltage Test 1240 V @ INPUT TERMINALS Over Voltage Protection YES Under Voltage Protection YES Weight 6.5 LBS. Cutout Size 10.75W x 7.25H Dimensions 12.25W x 8.875H x 5.625D UL & c UL Listed YES AC Distribution Specs: Rating 120 VAC/30 AMPS Breakers Max. 30 AMP Main... Up to 5 Branch Circuits DC Distribution Specs: DC Fuse Positions 2 @ 30 AMP max. each 10 @ 20 AMP max. each Reverse Polarity LED YES