PD4500 Inteli-Power Panel Specifications Table

PD4560 PD4590 Maximum DC Output Current 60-AMPS 90-AMPS Maximum Continuous Input Power 1,000 WATTS 1,550 WATTS No Load DC Output Voltage 13.6 VDC 13.6 VDC No Load Voltage Tolerance +/- .3 VDC +/- .3 VDC Full Load Output Voltage > 12.6 VDC > 12.6 VDC Ripple and Noise Voltage <50 MV RMS <50 MV RMS Input Voltage Tolerance 105 - 130 VAC 105 - 130 VAC Input Voltage Frequency 50-60 HZ 50-60 HZ Peak Inrush Current 47-AMPS 80-AMPS Efficiency (Typical) > 80% > 80% Reverse Battery Protection YES YES Electronic Current Limiting YES YES Cooling Fan Auto-variable speed Auto-variable speed Back Up Thermal Protection YES YES Full Function Charge Wizard YES YES Storage Temperature 20-80C 20-80C Operating Temperature 0-50C 0-50C Hipot Voltage Test <-------- 1240 V @ INPUT TERMINALS --------> Over Voltage Protection YES YES Under Voltage Protection YES YES Weight 10 LBS. 11 LBS. Cutout Size 10.125W x 13.25H 10.125W x 13.25H Dimensions 11.85W x 14.125H x 8.5D 11.85W x 14.125H x 8.5D UL & c UL Listed YES YES AC Distribution Specs: Rating 240 VAC/50 AMPS 240 VAC/50 AMPS Breakers Max. 50 AMP Main... Up to 12 Branch Circuits DC Distribution Specs: DC Fuse Positions 12/18 12/18 Blown Fuse Indicators Optional Optional Ground Bar Optional Optional